## Slide 1: WATERLESS TOILETS

## Slide 2: Presenter: Denis McCarthy mb: 0404 020 242 www.greentoilets.au waterless@greentoilets.au

## Slide 3: Tiny Homes Expo articles featured in Whole Life Times … get a free copy at Ecoflo Stall … or scan QR code

## Slide 4: Topics
Why choose a composting toilet?
Main principles of composting
Four composting phases
Types of waterless toilets
Installing
Starting

## Slide 5: Topics
Operating
Rotating
Mixing
Using composted waste
Models for Tiny Homes. Other Uses.
Q&A

## Slide 6: Why choose a composting toilet
Free of odours, chemicals, pumps
Low maintenance and electrical costs
Saves a typical household 35,000L of water per year
Hygienic method of recycling human waste

## Slide 7: Four main principles of composting
Aerobic bacteria breaks down waste much faster than anaerobic bacteria (smelly). The correct environmental conditions are needed for them to thrive.
1. 60% MOISTURE
2. AIRFLOW
60% of moisture content by weight. Too dry and the microbes will perish, too wet and conditions turn anaerobic.
Our systems incorporate ventilation and a fan or wind driven turbo vent, to encourage airflow for the oxygen-breathing microbes.

## Slide 8: Four main principles of composting
3. CARBON & NITROGEN
4. WARM TEMPERATURES
Microbes utilise carbon for energy and nitrogen to grow and reproduce.
A C:N ratio of 25:1 is good, hence carbon-rich bulking agent is recommended.
Microbes prefer warmer climates.
Composting slows and can eventually stop when the temperature drops below 18°C.

## Slide 9: Four phases of composting
1. Mesophilic Phase
Mesophilic organisms, which thrive between 20-30°C, break down the easily decomposable materials. The temperature increases as they proliferate.
2. Thermophilic Phase
Thermophilic organisms grow and thrive between 45-70°C. These rapidly decompose complex organic materials, generating high temperatures that kill pathogens.

## Slide 10: Four phases of composting
3. Cooling Phase
Mesophilic organisms return as it cools down. Actinobacteria and perhaps fungus and moulds decompose the larger, more complex material at a slower pace.
4. Curing Phase
Eventually any leftover pathogens are killed off. The pile matures into a humus, with the appearance and consistency similar to fresh potting mix.

## Slide 11: TYPES of waterless toilet systems
Split Systems
Clearance under the floor available
Self-Contained Systems
No clearance under the floor available
Batch
Continuous
Container
Extraction

## Slide 12: INSTALLING a split composting toilet
Clearance under the floor for the chamber
Vent above the roof
Leachate drain underground

## Slide 13: INSTALLING a “leachate drain”

## Slide 14: STARTING a composting toilet
Add a starter bed of bulking agent.
After a few days of pooing, add some microbes mixed with warm water.
Repeat step 2 in about 14 days.

## Slide 15: OPERATING a composting toilet
Add one generous cup of bulking agent
Spray enzyme solution around the pedestal
Close the lid
After every SOLID (POO) deposit:
After every LIQUID (PEE) deposit: Simply close the lid

## Slide 16: OPERATING a composting toilet
Do NOT dispose into the chamber:
Sanitary products and nappies
Chemical products or cleaning agents
Food waste

## Slide 17: MIXING a composting toilet
Flattens and aerates the compost pile
Accelerates the composting process
We recommend mixing batch systems around once a fortnight
The larger the system, the less often you would need to mix it

## Slide 18: ROTATING a batch composting toilet
1. Cover the compost pile with a shallow layer of bulking agent.
2. Add a starter bed to the new chamber, and place its lid onto the full chamber.

## Slide 19: ROTATING a batch composting toilet
3. Connect the new chamber.
4. Leave the full chamber in a sunny position to finish composting.

## Slide 20: USING finished compost
How can you tell if your compost pile is ready?
Appears slightly crumbly and moist with an earthy smell, similar to fresh potting mix.
No longer producing heat and will have reduced in size by about half.
Organic material and toilet paper should no longer be visible.
Where to use composted waste?
Bury it 10cm below ground around fruit or nut trees, lawns, flower beds and shrubs.
Avoid contact with edibles such as vegetables and herbs.

## Slide 21: NatureLoo™ ALECTURA : Comfort & Premium
Fully certified & approved in WA
Built specifically for tiny homes
Multi award winning innovative design
Full-time use up to 2-3 people.
Each optional extra chamber adds up to 2-3 people to its full-time capacity.

## Slide 22: NatureLoo™ ALECTURA : Comfort & Premium
Part-time use up to 4 people
Each optional extra chamber adds up to 4 people to its part-time capacity.
Comfort (no Ezylift)
Premium includes Ezylift

## Slide 23: NatureLoo™ ALECTURA : Comfort & Premium

## Slide 24: NatureLoo™ ALECTURA Comfort
December Sale Price
$1,595.00
Usual price $1,850.00
Save $255.00
Includes porcelain pedestal
Other inclusions see ecoflo.com.au/product/nature-loo-alectura-comfort/

## Slide 25: NatureLoo™ ALECTURA Premium composting toilet
December Sale Price
$1,995.00
Usual price $2,775.00
Save $780.00
Includes porcelain pedestal
Other inclusions see ecoflo.com.au/product/nature-loo-alectura-premium/
WA orders: sms 0404 020 242 em: waterless@greentoilets.au

## Slide 26: Bionova Self-Contained Composting Toilet
All-in-one, fully automatic, self contained composting toilet
Standard “Cabin” model $2,550.00
“Cabin Plus” model $2,650.00
ecoflo.com.au/product/bionova-self-contained-composting-toilet/
WA orders: sms 0404 020 242 em: waterless@greentoilets.au

## Slide 27: Bionova Self-Contained Composting Toilet
Uses: Caravans, Vans & RVs, Trucking, Mining, Tiny Homes, Boats, On-Slab, Shipping Containers
“Cabin” for 3 People (for full time use)
“Cabin Plus” for 3-5 People (FT use)
ecoflo.com.au/product/bionova-self-contained-composting-toilet/

## Slide 28: Other Uses … of Alectura, Bionova & other models
RVs and Vans
Caravans
Tour Buses
Walking Trails
National Parks
Wineries
Mines Sites
Sport Clubs
Cemeteries
Residential
Remote communities

## Slide 29: Questions?

## Slide 30: WA: Denis McCarthy mb: 0404 020 242 www.greentoilets.au waterless@greentoilets.au

## Slide 31: Thanks for listening!